## Slide 1: Chapter 2
Conducted and Radiated Media
Jill West | Curt M. White, Data Communications and Computer Networks: A Business User’s Approach, 9th Edition. © 2023 Cengage. All Rights Reserved. May not be scanned, copied or duplicated, or posted to a publicly accessible website, in whole or in part.

## Slide 2: After reading this chapter, you should be able to:
Identify common cabling standards
Compare types of network cables
Compare wireless network technologies
Evaluate the best media for network connections

## Slide 3: Introduction
The world of computer networks would not exist if there were no medium by which to transfer data
The two major categories of media include:
  Conducted (wired) media
    standards for cables and connectors
  Radiated (wireless) media
    standards for transmission
Media selection criteria

## Slide 4: Cabling Standards (1 of 3)
The need for agreement between network devices starts with the definition of standards for physical equipment
Components:
  electrical components
  mechanical components
  functional components
  procedural components

## Slide 5: Cabling Standards (2 of 3)
Personal Area Network (PAN) Connector Standards
  USB Type-A
  USB Type-B
  USB Type-B Micro
  USB-C
  Lightning

## Slide 6: Cabling Standards (3 of 3)
Personal Area Network (PAN) Protocol Standards:
  USB 1.0
  USB 2.0
  USB 3.0
  Thunderbolt

## Slide 7: Twisted Pair Wire (1 of 5)
One or more pairs of single conductor wires that have been twisted around each other
Twisted pair wire is classified by category. Twisted pair is currently Category 1 through Category 8, although Categories 1, 2, 3, and 4 are nearly obsolete
Twisting the wires helps to eliminate electromagnetic interference between the two wires
Shielding can further help to eliminate interference

## Slide 8: Twisted Pair Wire (2 of 5)

## Slide 9: Twisted Pair Wire (3 of 5)

## Slide 10: Twisted Pair Wire (4 of 5)

## Slide 11: Twisted Pair Wire (5 of 5)
Table 2-1 Characteristics of twisted pair cables
UTP Category | Typical Use | Maximum Data | Maximum Transmission Range | Advantages | Disadvantages
Cat 5 | LANs | 100 Mbps (100 MHz) | 100 m (328 ft) | Inexpensive, easy to install and interface | Security, noise, obsolete
Cat 5e | LANs | 250 Mbps per pair (125 MHz) | 100 m (328 ft) | Inexpensive, easy to install and interface, supports Gigabit Ethernet | Security, noise
Cat 6 | LANs | 250 Mbps per pair (250 MHz) | 100 m (328 ft) | Higher data rates than Cat 5e, less noise | Security, noise
Cat 6a | LANs | 500 MHz | 100 m (328 ft) | Support for 10 Gig Ethernet, increased shielding | Security, noise
Cat 7 | Backbone connections | 600 MHz | 100 m (328 ft) | 100 Gig Ethernet at very short distances (15 m) | Security, cost, requires special connectors
Cat 7a | Backbone connections | 1000 MHz | 100 m (328 ft) | Same as Cat 7, plus additional shielding | Security, cost, requires special connectors, thicker and more difficult to install
Cat 8 Class I and Class II | Backbone connections | 2000 MHz | 30 m (98 ft) | 25 Gig and 40 Gig support at longer distances than Cat 7; Cat 8 Class I uses standard connectors | Security, cost

## Slide 12: Twisted Pair Summary
Most common form of wire
Relatively inexpensive
Easy to install
Carries high data rates (but not the highest)
Can suffer from electromagnetic noise
Can be easily wire-tapped
Comes in shielded and unshielded forms

## Slide 13: Coaxial Cable (1 of 3)
A single wire wrapped in a foam insulation surrounded by a braided metal shield, then covered in a plastic jacket.
Cable comes in various thicknesses
Baseband coaxial technology uses digital signaling in which the cable carries only one channel of digital data
Broadband coaxial technology transmits analog signals and is capable of supporting multiple channels

## Slide 14: Coaxial Cable (2 of 3)

## Slide 15: Coaxial Cable (3 of 3)

## Slide 16: Coaxial Cable Summary
A single wire surrounded by a braided shield
Because of shielding, can carry a wide bandwidth of frequencies
Thus, is good with applications such as cable television
Not as easy to install as twisted pair
More expensive than twisted pair

## Slide 17: Fiber-Optic Cable (1 of 7)
A thin glass cable approximately a little thicker than a human hair surrounded by a plastic coating and packaged into an insulated cable
A photo diode or laser generates pulses of light which travel down the fiber optic cable and are received by a photoreceptor

## Slide 18: Fiber-Optic Cable (2 of 7)

## Slide 19: Fiber-Optic Cable (3 of 7)
Fiber-optic cable is capable of supporting millions of bits per second for 1000s of meters
Thick cable (62.5/125 microns) causes more ray collisions, so you have to transmit slower. This is step index multimode fiber. Typically use LED for light source, shorter distance transmissions
Thin cable (8.3/125 microns) – very little reflection, fast transmission, typically uses a laser, longer transmission distances; known as single mode fiber

## Slide 20: Fiber-Optic Cable (4 of 7)

## Slide 21: Fiber-Optic Cable (5 of 7)
Fiber-optic cable is susceptible to reflection (where the light source bounces around inside the cable) and refraction (where the light source passes out of the core and into the surrounding cladding)
Thus, fiber-optic cable is not perfect either. Noise is still a potential problem

## Slide 22: Fiber-Optic Cable (6 of 7)

## Slide 23: Fiber-Optic Cable (7 of 7)

## Slide 24: Fiber-Optic Cable Summary
Fiber optic cable can carry the highest data rate for the longest distances
Initial cost-wise, more expensive than twisted pair, but less than coaxial cable
But when you consider the superiority of fiber, initial costs outweighed by capacities
Need two fibers for a round-trip connection
Not affected by electromagnetic noise and cannot be easily wiretapped, but still noise

## Slide 25: Conducted Media
Table 2-4 A summary of the characteristics of conducted media
Type of Conducted Medium | Typical Use | Maximum Data Rate | Maximum Transmission Range | Advantages | Disadvantages
Twisted pair Cat 5, 5e, 6, 6a, 7, 7a, 8 | LANs | 100 Mbps-100 Gbps | 100 m (328 feet) | Inexpensive, versatile | Noise, security
Coaxial cable | Cable TV, long-distance telephone, short-run computer system links | 1 Gbps | 5-6 kilometers (3-4 miles) (at lower data rates) | Low noise, multiple channels | Security
LED fiber optic | Data, video, audio, LANs | 10 Gbps | 300 meters (approx. 1000 feet) | Secure, high capacity, low noise | Expensive interface but decreasing in cost
Laser fiber optic | Data, video, audio, LANs, WANs, MANs | 100s Gbps | 100 kilometers (approx. 60 miles) | Secure, high capacity, very low noise | Expensive interface

## Slide 26: Radiated Media on LANs (1 of 2)
Radio, satellite transmissions, and infrared light are all different forms of electromagnetic waves that are used to transmit data
Technically speaking – in wireless transmissions, space is the medium
Note in the following figure how each source occupies a different set of frequencies

## Slide 27: Radiated Media on LANs (2 of 2)

## Slide 28: Wi-Fi (1 of 4)
Wireless LAN, often referred to by the trademarked term Wi-Fi (wireless fidelity)
Constituents:
  Wireless clients
    desktops, laptops, mobile devices, etc.
  A wired LAN
  Access point, a.k.a, wireless router

## Slide 29: Wi-Fi (2 of 4)

## Slide 30: Wi-Fi (3 of 4)

## Slide 31: Wi-Fi (4 of 4)
Table 2-5 Technical details for 802.11 wireless standards
Standard | Frequency Band | Maximum Theoretical Throughput | Geographic Range
802.11b (Wi-Fi 1) | 2.4 GHz | 11 Mbps | 100 m
802.11 a (VVi-Fi 2) | 5 GHz | 54 Mbps | 50 m
802.11g (Wi-Fi 3) | 2.4 GHz | 54 Mbps | 100 m
802.11 n (Wi-Fi 4) | 2.4 GHz or 5 GHz | 600 Mbps | Indoor: 70 m Outdoor: 250 m
802.11ac (Wi-Fi 5) | 5 GHz | Wave 1 (3 data streams): 1.3 Gbps Wave 2 (4 data streams): 3.47 Gbps Wave 3 (8 data streams): 6.93 Gbps | Indoor: 70 m Outdoor: 250 m
802.11 ax (Wi-Fi 6 and Wi-Fi 6E) | 2.4 GHz or 5 GHz or (Wi-Fi 6E only) 6 GHz | 9.6 Gbps | Indoor: 70 m Outdoor: 250 m

## Slide 32: Bluetooth (1 of 2)
Bluetooth protocol was created to unify separate nodes as mobile devices, computers, and accessories within a smaller range than the Wi-Fi standards
A wireless technology that uses low-power, short-range radio frequencies to communicate between devices
Bluetooth can transmit through solid, non-metal objects

## Slide 33: Bluetooth (2 of 2)
Its typical link range is from 10 cm to 10 m, but can be extended to 100 m by increasing the power
Class 1 devices: transmission of data up to 100 meters
  computers
Class 2 devices: transmission of data up to 10 meters
  mobile devices, headphones, etc.
Class 3 devices: transmission of data up to a couple of meters
  mouses and keyboards

## Slide 34: Zigbee (1 of 2)
New wireless technology designed for data transmission between smaller, often embedded, devices
Low data transfer rates (20–250 Kbps) and corresponding low power consumption
Bluetooth is best at replacing cables for short distances, while Zigbee is good at sending low-speed and low-power signals over short to medium distances

## Slide 35: ZigBee (2 of 2)
Based upon IEEE 802.15.4 standard
Ideal for heating, cooling, security, lighting, and smoke and CO detector systems
ZigBee can use a mesh design – a ZigBee-enabled device can both accept and then pass on ZigBee signals

## Slide 36: Ultra-Wideband (1 of 2)
Ultra-wideband
  UWB not limited to a fixed bandwidth but broadcasts over a wide range of frequencies simultaneously
  Many of these frequencies are used by other sources, but UWB uses such low power that it “should not” interfere with these other sources
  Can achieve speeds up to 100 Mbps but for small distances such as wireless LANs

## Slide 37: Ultra-Wideband (2 of 2)
Ultra-wideband (continued)
  Proponents for UWB say it gets something for nothing, since it shares frequencies with other sources. Opponents disagree
  Cell phone industry against UWB because CDMA most susceptible to interference of UWB
  GPS may also be affected
  One solution may be to have two types of systems – one for indoors (stronger) and one for outdoors (1/10 the power)

## Slide 38: Infrared Transmissions
Transmissions that use a focused ray of light in the infrared frequency range
Very common with remote control devices, but can also be used for device-to-device transfers, such as PDA to computer

## Slide 39: Near-Field Communications
Very close distances or devices touching
Magnetic induction (such as radio frequency ID) used for transmission of data
Commonly used for data transmission between cellphones (non-Apple devices)

## Slide 40: Summary of Wireless LAN Technologies
Table 2-6 Summary of wireless media
Type of Wireless Medium | Typical Use | Maximum Data Transfer Rate | Typical transmission Range | Advantages | Disadvantages
Wi-Fi | Local area networks | 10 Gbps | 45-90 meters (150-300 feet) | Relative ease of use | Several standards
Bluetooth | Short-distance transfer | 2 Mbps | A few feet to 100 meters (328 feet) depending on device class | Universal protocol | Limited distances
Zigbee | Short-to-medium distance, low- speed transfers | 250 Kbps | Almost unlimited distance (mesh) | Low power | Low transfer speeds
IR | Short-distance data transfer | Varies by protocol used | 10 meters (33 feet) | Fast, inexpensive, secure | Short distances, line of sight
UWB | Short-distance, high-speed transfers; location discovery | 100 Mbps | 100 meters (328 feet) | High speed, not restricted to fixed frequencies | May interfere with other sources
NFC | Very short distance data transfer | 424 Kbps | About 4 cm | High-speed connections; allows for passive devices with no internal power supply | Very limited distance

## Slide 41: Media Selection Criteria
Cost
Speed
Distance and expandability
Environment
Security

## Slide 42: Cost
Different types of costs
  Initial cost – what does a particular type of medium cost to purchase? To install?
  Maintenance / support cost
ROI (return on investment) – if one medium is cheaper to purchase and install but is not cost effective, where are the savings?

## Slide 43: Speed
Two different forms of speed:
  Propagation speed – the time to send the first bit across the medium
    This speed depends upon the medium
    Airwaves and fiber are speed of light
    Copper wire is two thirds the speed of light
  Data transfer speed – the time to transmit the rest of the bits in the message
    This speed is measured in bits per second

## Slide 44: Expandability and Distance
Certain media lend themselves more easily to expansion
Don’t forget right-of-way issue for conducted media and line-of-sight for certain wireless media

## Slide 45: Environment
Many types of environments are hazardous to certain media
  Electromagnetic noise
  Scintillation and movement
  Extreme environmental conditions

## Slide 46: Security
If data must be secure during transmission, it is important that the medium not be easy to tap
  Make the wire impervious to electromagnetic wiretapping
  Encrypt the signal going over the medium

## Slide 47: Summary (1 of 2)
All data communication media can be divided into two basic categories: conducted (wired) media, and radiated (wireless) media
Cabling standards define both physical and logical (protocols) standards
The three types of conducted media are twisted pair, coaxial cable, and fiber-optic cable
Twisted pair and coaxial cable are both metal wires and are subject to electromagnetic interference
Fiber-optic cable is a glass wire and is impervious to electromagnetic interference

## Slide 48: Summary (2 of 2)
Several basic groups of wireless media exist: Wi-Fi, Bluetooth, ZigBee, ultra-wideband, near-field communications, and infrared
Each of the wireless technologies is designed for specific applications
When trying to select a particular medium for an application, it helps to compare the different media using these criteria: cost, speed, expandability and distance, environment, and security